## Slide 1: EEE MSc Project Guidance notes
Part 6/6

## Slide 2: Measurements and errors
Plot graph and fit e.g. straight line y = mx + c
Automatic averaging, estimate of random errors, presence of systematic errors.
Straight line easiest, usual to derive linear form of non linear fits, e.g. x = ½gt2
→ x/t = ½gt, gradient = ½g
x/t
t
x
t
y
x
x
x
x
x
x
Notes: There is more information on a graph than just the gradient. e.g. intercepts – Think what the equation is telling you.

## Slide 3: e.g. Arrhenius equation
lntf
1/kT
x
x
x
Plot lntf versus 1/kT
Slope,
Intercept,

## Slide 4: Errors
Experiments measure a previously unknown quantity or test a theory. We cannot know for sure unless error (uncertainty) is known
e.g. Diameter of a rod fitting through a hole exactly 3cm diameter is measured as 2.99cm
If diameter is (2.99 ± 0.03) cm we are in trouble!
Error must be determined within experiment.
e.g. Don’t say R = (10.5 ± 0.5) Ω just because theory says R = 10 Ω.
Notes: Error must be determined within the experiment. Don’t make it up as you know what it should be!

## Slide 5
Error tells how reproducible results are (spread of values) – STATISTICAL ERROR
Distinguished from SYSTEMATIC ERROR
If many measurements, take σ of Gaussian spread of values
Usually only need rough estimate:
Instrumental
Graphical
Numerical
Notes: Systematic error, e.g. a scale is 1% wrong contributing a 1% error to each measurement, not apparent from spread of values.

## Slide 6: 1) Instrumental
Resolution based
e.g.1. DVM res. = 0.1V so error is ± (½ least count) = 0.05V
e.g.2. Determined by number of counts that can be displayed, determined by the number of digits.
4 ½ digits means 4 digits with 0-9 variation and one leading digit which is 0 or ±1. Total of 20000 counts.
Resolution = smallest count / maximum count, i.e. 1/20000 or ±0.005% for a 4 ½ display.
e.g. Specification of ±(0.05% + 1 count) for a 4 ½ digit DMM reading 10.000 Volts, Corresponds to: ±0.05% of 10 Volts = ± 0.005V = ± 5mV, ±1 count of XX.XXX display = ± 0.001 V = ± 1mV
Total error of ± (5mV+1mV) = ± 6mV.
Notes: Resolution = smallest interval measurable

## Slide 7
Accuracy (how close to true value)
e.g. ammeter with ± 5% reading 1A could be 0.95 to 1.05A
Analogue meters – accuracy as % of f.s.d
e.g. 1A measured on 3A fsd range with ±5% fsd accuracy → ± 0.15A
(so measuring 0.2A on this range is ± 75%!)
Digital meters – accuracy as % of reading plus % of range

## Slide 8: 2) Graphical
Draw best line through data
For estimate of error on gradient, draw lines of max. and min. gradient
y
x
x
x
x
x
x
m = 10.7, 8.9, 11.9
So m = 10.7 ± 1.5
c = 6.9, 13, 0
So c = 7 ± 7
Notes: Best line through data – approximately equal spread of data points above and below line.

## Slide 9
When using error bars
y
x
Errors on individual measurements taken into account

## Slide 10: 3) Numerical method
Uses mean, standard deviation
Errors on derived quantities
Relate error on final result to error on measured quantities.
Constant factors –
e.g r ± δr, C = 2πr ± 2πδr i.e. same fractional error
Notes: Often the quantity we want has to be calculated from one or a number of measured parameters.

## Slide 11
2) Powers-
e.g. if square has side x ± δx, area = (x ± δx)2 so x2 ± 2xδx
3) Multiplication/division of independent measurements:
4) Addition/subtraction: If L = a + b
(δL)2 = (δa)2 + (δb)2 i.e. absolute error, not fractional error

## Slide 12
Finally.
Don’t double count errors -
errors on individual measurements are already included in errors on gradient or intercept. There is no need to add the individual errors to the errors on fitted results!

## Slide 13: Errors - Further reading
“Experimental Methods”. L. Kirkup. John Wiley & Sons. 1994